## Slide 1
Korean Nuclear Energy Activities
Sep. 27, 2023
Bum-Jin CHUNG
Korean Nuclear Society
(Kyung Hee University)

## Slide 2: Energy Imports of Korea
Korea lacks natural resources including renewable resources
  imports 95% of energy
  corresponds to 25% national import
  corresponds to the profits from semiconductor and auto exports: Two major export areas of Korea
Annual Energy Imports: ~100 billion$
Breakdown : Oil (73.1%), LNG (18.8%), Coal (9.9), Uranium(0.9%)

## Slide 3: Nuclear Power Plants in Korea
Seoul
Hanbit
6 units
Kori
4 units
Shin-Kori
6 units
Wolsong
4 units
Shin-Wolsong
2 units
Hanul
6 units
Shin-Hanul
4 units
In Operation
Under Construction
Under Planning
25 NPPs in operation (2023)
3 units under construction
Kori #1 and Wolsong # 1 shutdown permanently
4 planned NPPs canceled
2 NPP constructions suspended
(Resume construction soon)
Yongkwang→ Hanbit
Uljin → Hanul
Chunji, Daejin
4 units
Electricity cost (~110 \/kWh) and share
Nuclear ~60 \/kWh (30%)
Coal ~80 \/kWh (40%) → 150 W/kWh
LNG ~120 \/kWh (20%) → 280 W/kWh
Others ~200 \/kWh (10%) → 270 W/kWh
Permanent shutdown
Notes: • Korea has 24 nuclear power plants in operation at four sites as you see in this slide.
• Among them 20 units are Pressurized Water Reactors (PWR), and the others are Pressurized Heavy Water Reactors.
• Nuclear power, providing one-third of total electricity in Korea, has been a key for the Korean economy and energy security.

## Slide 4
Continuous construction over 30 years
High-quality system
Self-reliance of A/E, Equipment, Fuel
Gradual localization of BOP
World best constructors
Rich experience in overseas projects
such as Burj Khalifa
6
KEPCO
KHNP
KEPCO
NF
KEPCO
E&C
KEPCO
KPS
KAERI
Construction Co.
DOOSAN
NUCLEAR
FUEL SUPPLY
A/E + NSSS
DESIGN
EQUIPMENT
SUPPLY
PLANT
MAINTENANCE
R & D
CONSTURUCTION
NUCLEAR UTILITY
PROJECT MANAGEMENT
& COMMISSIONING
Supply Chain for Nuclear Project

## Slide 5
2009
Won contracts
for a JRTR in Jordan, and 4 APR1400 in the UAE (Successful construction)
Advanced Reactor Development
of APR1400 and SMART
2000
Establishment of Nuclear Safety
and Security Commission (NSSC)
2011
1990
Technology Self-Reliance
Development
of OPR1000
1959
Establishment of Office of Atomic Energy & Atomic Energy Research Institute
1958
Enactment of
Atomic Energy Act
1970
Introduction of
Nuclear Power
Construction of
Kori Unit 1
(’71~78)
Construction of
The first Research
Reactor, TRIGA
Mark II
1962
Establishment of Localization
Plan (’84)
1980
2012
Acquired Standard Design Approval for SMART
2015
Signed SMART PPE with Saudi
Korean Nuclear Energy at a Glance
Notes: 한국은 1950년대 말, 관련 법령을 제정하고 조직을 설립하는 등 꾸준히 원자력발전 관련 기술개발에 투자하였으며 1962년 트리가마크 II 연구용원자로를 건설한 바 있습니다.
Let me start by saying the brief history about nuclear energy in Korea. In the late 1950’s, Korea made a steady effort in developing nuclear R&D like promulgating series of atomic energy laws together with the nuclear organizations. Moreover, a small research reactor TRIGA Mark-II was constructed in 1962.
1978년 첫번째 상업용 원전을 건설하였으며, 뒤이어 1980년대에 핵연료 국산화에 성공하게 됩니다. 또한 정부의 지속적인 투자와 연구진들의 끊임없는 노력으로 APR 1400과 SMART 개발에 성공하여 ’09년 UAE에 APR 1400 모델 수출 및 2015년 9월에는 사우디에서 스마트 원전 건설 전 상세설계(PPE, Pre-Project Engineering)협약을 체결하게 되었습니다.
Kori Unit 1, nation’s first NPP supplied by the US Westinghouse turnkey project, went into commercial operation in 1978 followed by the successful localization of nuclear fuels for pressurized heavy water in the 1980’s. After the constant pursuit of investment from the government coupled with the efforts by nuclear industries, academia and research institutes, the painstaking efforts finally began to bear fruit as Korea developed APR 1400 and SMAR, small-Medium sized reactor, followed by the export of New Korean PWR model, APR 1400, to the United Arab Emirates in 2009, the first turnkey project nuclear export from Korea.
In addition, Korea signed the SMART PPE agreement with Saudi Arabia in September 2015

## Slide 6
Nuclear Phase-out policy declared at the permanent shutdown ceremony of Kori #1:
  Reduction of nuclear and coal portions
  Expansion of renewables
  (de facto expansion of LNG)
  Cancellation of 4 planned NPPs
  Suspension of 4 NPPs in construction
  (Shin-Kori 5&6, Shin-Hanul 3&4)
Huge protests from the nuclear society, the press, opposition parties, etc.
  Several brave professors have stood against the policy.
Current situation
  70% of the public continuously show pro-nuclear views.
  Realities of the renewables have been recognized. (Undespatchability, Intermittency, Electricity instability, High cost, Land devastation, etc.)
  Positive recognition enhanced for nuclear power as the clean energy source tackling climate change.
  New President Yoon declared ‘Scrapping nuclear phase-out policy’.
Phasing out Nuclear Declaration(2017. 6. 19)
Energy Transition Policy

## Slide 7
2019 Energy consumption by form
  Electricity (44.8 million TOE) from nuclear, coal, oil, LNG, renewables, etc
  Fossil fuels (186.6 million TOE) from coal, oil, LNG, etc.
  → Net Zero required for Fossil fuels (4 times larger than electricity) as well.
  → Transition to Electricity and/or Hydrogen (Carriers) required.
  (Carbon free electricity and Carbon free hydrogen?)
2019 Energy consumption by sector
  Industry (142.9 million TOE), Transportation (43 million TOE), Home (22.6 million TOE), Commercial (17.5 million TOE), Public (5.4 million TOE)
  Almost impossible to achieve NZE without sacrificing industry and commercial sectors (70%).
‘Carbon Free 2050’ Plan of Korea
  Unrealistic (Renewable deployment, Hydrogen import, Super-grid connection,
  Based on Nuclear Phase-out premise
  Cost not calculated (Tremendous)
  → Possible only the renewables are substituted by nuclear.
Net Zero Emission (CO2 free)

## Slide 8: Role of the Nuclear in Korea
11
Energy Reserve (Energy Security)
Oil : 3.5 months
LNG : 1.5 months
Coal : 0.5 days
Nuclear : 18 months (+10 month)
Independent Grid
Comparison
1g U235
9 drum Oil
3 tons of coal

## Slide 9: Nuclear Exports
Barakah NPPs in 2009
(Exported with WH)
JRTR in 2009
Jordanian Research and Training Reactor

## Slide 10: APR1400 Competitiveness
UAE Export 2009 (4 Barakah units)
Economic competitiveness
EU Requirement (Sep. 26, 2017)
NRC Design Certificate (Aug. 26, 2019)
UAE construction record : ‘In-Time’ ‘Within Budget’

## Slide 11
VHTR
Hydrogen Plant
Innovative Nuclear System
SMART &
(PPE Saudi Arabia)
i-SMR
SFR fuel cycle
(Sodium-cooled Fast Reactor + Pyroprocess)
Long-Term
APR+
(Construction Pending)
APR1000
APR1400
(EU R. Oct. 2017)
(NRC DC Sep.2018)
Now
Near-Term
NHDD
(Nuclear Hydrogen development and demonstration)
Current and Future NPP Development

## Slide 12: Korean Nuclear Society
Established in 1969.
Members : ~ 6,000
Objectives
  Contribute to the advancement of nuclear engineering and technology
  Promote the peaceful use of nuclear energy and radiation
  Promote cooperation between members
Activities
  Host KNS conferences (2 times a year)
  Foster & coordinate the activities of professional divisions
  Conduct research, consultation & evaluation of projects
  Cooperate with other organizations having similar aims
  sponsoring international conferences and workshops
  Publish academic journal (Nuclear Engineering & Technology)
  Encourage members by honors and awards
  Foster nuclear engineering education both domestic & international students (scholarship to young students)

## Slide 13: Organization
(Board of Directors)
1 President
1 Chief vice-president (elected)
5 vice-presidents (nominated)
20 Secretaries
2 Auditors
(Members)
~260 Board of Trustees
~6,000 Members
12 Research divisions
Several committees
1 High level policy institute

## Slide 14: Major Activities
(Internal)
Spring/Autumn Conferences
NET journal
Awards
Scholarships
Nuclear policy institutes
(External)
Public education
Press releases
Policy statements

## Slide 15: NET and its JIF and Rank
Chart: 
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
JIF | 0.991 | 0.465 | 0.487 | 0.576 | 0.758 | 0.77 | 0.792 | 1.144 | 1.655 | 1.546 | 1.846 | 2.341 | 2.817 | 2.7
Rank | 12 | 27 | 27 | 23 | 21 | 21 | 23 | 15 | 4 | 7 | 6 | 5 | 6 | 5

## Slide 16: Nuclear Journal Rank
1 | INTERNATIONAL JOURNAL OF ENERGY RESEARCH | 4.6
2 | JOURNAL OF NUCLEAR MATERIALS | 3.1
3 | RADIATION PHYSICS AND CHEMISTRY | 2.9
4 | Nuclear Science and Techniques | 2.8
5 | Nuclear Engineering and Technology | 2.7
6 | Progress in Nuclear Energy | 2.7
7 | INTERNATIONAL JOURNAL OF RADIATION BIOLOGY | 2.6
8 | Nuclear Materials and Energy | 2.6
9 | HEALTH PHYSICS | 2.2
10 | RADIATION MEASUREMENTS | 2
11 | ANNALS OF NUCLEAR ENERGY | 1.9
12 | IEEE TRANSACTIONS ON NUCLEAR SCIENCE | 1.8
13 | RADIOCHIMICA ACTA | 1.8
14 | FUSION ENGINEERING AND DESIGN | 1.7
15 | NUCLEAR ENGINEERING AND DESIGN | 1.7
16 | Applied Radiation and Isotopes | 1.6
17 | JOURNAL OF RADIOANALYTICAL AND NUCLEAR CHEMISTRY | 1.6
18 | JOURNAL OF RADIOLOGICAL PROTECTION | 1.5
19 | NUCLEAR TECHNOLOGY | 1.5
20 | NUCLEAR INSTRUMENTS & METHODS IN PHYSICS RESEARCH SECTION A-ACCELERATORS SPECTROMETERS DETECTORS AND ASSOCIATED EQUIPMENT | 1.4
21 | NUCLEAR INSTRUMENTS & METHODS IN PHYSICS RESEARCH SECTION B-BEAM INTERACTIONS WITH MATERIALS AND ATOMS | 1.3
22 | JOURNAL OF NUCLEAR SCIENCE AND TECHNOLOGY | 1.2
23 | NUCLEAR SCIENCE AND ENGINEERING | 1.2
24 | Nuclear Technology & Radiation Protection | 1.2
25 | JOURNAL OF FUSION ENERGY | 1.1
26 | RADIOPROTECTION | 1.1
27 | Science and Technology of Nuclear Installations | 1.1
28 | Radiation Effects and Defects in Solids | 1
29 | RADIATION PROTECTION DOSIMETRY | 1
30 | FUSION SCIENCE AND TECHNOLOGY | 0.9
31 | NUCLEAR ENGINEERING INTERNATIONAL | 0.6
32 | ATOMIC ENERGY | 0.5
33 | KERNTECHNIK | 0.5
34 | ATW-INTERNATIONAL JOURNAL FOR NUCLEAR POWER | 0.1

## Slide 17: K-SMRs
1997
2012
SMART Project Initiation
SMART Standard Design Approval
SMART Safety Enhancement Project
Korea-Saudi Arabia SMART partnership
BANDI Conceptual Design
MMR CNL Demonstration Project (USNC)
PGSFR Basic Design
i-SMR Project Initiation
BANDI Conceptual Design
SMART100 Standard Design Approval
2014
2015
2016
2018
2020
2021
2022
2023
USNC MMR
i-SMR
PGSFR
SMART
BANDI

## Slide 18: SMART(System-integrated Modular Advanced ReacTor)
  For Electricity Generation and District Heating or Desalination
Electricity
Hot Water Heat supply
Fresh Water
Desalination Plant
Sea Water
Steam
Steam Transformer

## Slide 19: SMART Design Characteristics
  SMART Reactor Assembly
Thermal Power : 365 MWt
Electric Power : 110 MWe
Desalination : 40,000 ton/day
Design Life : 60 years
Design Pressure : 17 MPa
Operating Pressure : 15 MPa
Design Temperature : 360 ℃
Core Inlet/Outlet Temperature : 295.5/322 ℃
Fuel Type : 17×17 Square FA
Fuel Material : UO2 (＜5.0 w/o)
Active Core Height : 2.0 m
Refueling Cycle : 36 months
  General Information
  Reactor Coolant System
  Fuel and Reactor Core

## Slide 20: SMART Development
  Standard
  Design Approval
09.1~12.6
  2012
  2007
Basic
Design
99.4~02.3
SMART
Prototype
02.7~06.2
Conceptual
Design
97.7~99.3
Pre - Project
Service
06.7~07.6
  1999
  2006
  2002
  1997
  Safety
  Enhancement
12~15
  2009
  2022
  2019
  2016
  SMART
  PPE
15.12~18.11
  SMART
  SDCA
19.1~12.12
  2008
  Technology
  Optimization
07.7~08.12

## Slide 21: Comprehensive Technology Validation and SDA
15
  Fuel TH Tests
  Mechanics and Components
  Thermal - Hydraulics Experiment
CHF Measurement Test
Fuel Performance Tests
TEST Fuel
Vibration TEST
Measurements
TEST Section
Spacer Grid
TEST Section
RPV Dynamics Test, RCP Mockup Test and Helical ISI Test
Dynamic Test
RCP TEST Loop
SG Tube Material (A690) Irradiation Test
Test Facility
Low Friction Cable
VISTA Integral Test Facility
PRHRS Heat Ex.
Safety Injection
Pressurizer
World’s Unique and Largest Full Scope Accident Simulation
1:1 Height, 1/49 Volume
  SMART - ITL
  SMART - MCR Simulator
Instructor
Supervisory Operator
Operator
Systems, Component, and Design Tools have been fully Developed and Licensed
  SMART Standard Design Approval in 2012 (Meet the Most Country’s Licensing Requirements)

## Slide 22: SMART FOAK Design

## Slide 23: i-SMR Design Characteristics - RCS

## Slide 24
i-SMR Safety Systems
Passive Auxiliary Feedwater System (PAFS)
Passive Emergency Core Cooling System (PECCS)
Passive Containment Cooling System (PCCS)
03

## Slide 25
i-SMR Development Roadmap
12
Standard Design Approval (in Korea) by 2028
Government funding has been started for standard design program this year.
Pre-design review of Korean regulatory body has been already started in July.
SDA acquisition by 2028 and first module installation by 2031
03

## Slide 26: i-SMR Reactor and Major Components
TM-ICI
IV-CEDM
Canned Motor RCP
CSB
IBA
UGS
FA support
IV-CEDM support and Cable penetration
Control rod guide and FA support
Canned Motor Pump(no mechanical seal, No leakage detection system)
Helical coil once-through steam generator
Steam Pressurizer
Helical SG

## Slide 27: i-SMR Innovative Technologies

## Slide 28
BANDI – Marine-based NPP
13
‘Block-type’ reactor coolant system where the reactor vessel the steam generator are ‘nozzle-to-nozzle’ connected to each other without big pipes.
The first phase of the conceptual design of BANDI was started in 2016 and completed in 2022. The second phase will be continued from 2023 to 2028.
03

## Slide 29: Sodium-Cooled Fast Reactor (SALUS-100)
• Completion of SFR (PGSFR) engineering design for TRU burning and core technology development for safety verification
• Development of power generation SMR (SALUS-100) in order to enter the overseas SMR market
※ Canadian vendor review application and technical and business cooperation with ARC

## Slide 30: High Temperature Gas Cooled Reactor (MMR++)
• Completed nuclear reactor key-technology development for supplying high-temperature heat necessary for hydrogen production
• Discussion on demonstration reactor linked to industrial process heat and high-temperature water electrolysis hydrogen production unit (MMR++)
※ KAERI provides reactor design (core design and safety analysis)

## Slide 31: MSR, Molten Salt Reactor
• Selected as “Innovation Challenge Project” in 2021 to secure MSR’s key technology suitable for carbon-free marine systems (’23-’26)
• Development of mobile molten salt reactor (MSR) technology for floating or ship propulsion through industry-academia-research cooperation
※ Joint planning with Samsung Heavy Industries is underway
He Pump
Pump
HX
Dump Tank
Plug